## Slide 1
Tiny ECG Classification on ESP32
A 23 KiB full-int8 CNN with 95.1% test accuracy and 52.09 ms ESP32 inference
Aleksandar Toslev | Luka Zotovikj
Heidelberg University | Beginner's Practical Neural Networks from Scratch | 2026
FROM-SCRATCH CNN / TFLITE MICRO
Project Goal 🎯
Develop a 1D CNN from scratch in NumPy to accurately classify different heartbeat types, apply INT8 quantization to reduce the model size, and optimize it for efficient deployment on an ESP32.
95.12%
INT8 TEST ACCURACY
73.9%
SMALLER MODEL
52.09 ms
ESP32 MEAN INFERENCE / BEAT
1. Heartbeat data are highly imbalanced
Five heartbeat types must be separated from 187-point ECG segments. Normal beats dominate training, so overall accuracy alone can hide minority-class failure.
Representative normalized beats
Stored 0-1 amplitudes; flat tails are zero-padding. One real training sample per class.
Source: PhysioNet MIT-BIH; Kachuee et al. (2018).
Training class distribution
Chart: 
| N | S | V | F | Q
Training beats | 61600 | 1889 | 4920 | 545 | 5466
F has 113x fewer training beats than N.
Stable convergence without clear overfitting
Chart: Epoch
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Train | 1.1661 | 0.75098 | 0.61628 | 0.54929 | 0.50009 | 0.46597 | 0.42431 | 0.38715 | 0.36764 | 0.35398 | 0.33044 | 0.32557 | 0.31348 | 0.3039 | 0.29921 | 0.29164 | 0.28701 | 0.27609 | 0.27099 | 0.26546
Validation | 0.80136 | 0.58137 | 0.51936 | 0.45543 | 0.43849 | 0.39706 | 0.36001 | 0.34399 | 0.31773 | 0.29649 | 0.29385 | 0.28887 | 0.2668 | 0.26672 | 0.25911 | 0.25444 | 0.2518 | 0.25686 | 0.24332 | 0.26813
2. Compact CNN, explicit imbalance controls
The complete forward pass, backward pass, weighted loss, and Adam updates are implemented in NumPy. Keras is used only as an export bridge.
11,173 trainable parameters
187 x 1 ECG beat
normalized heartbeat segment
Three convolution blocks
16 (k=7) -> 32 (k=5) -> 64 (k=3)
Global average pooling
small representation, no large flatten layer
Dense 32 + dropout
compact nonlinear classifier
Five-class softmax
N / S / V / F / Q
Three complementary strategies
1
Capped class-weighted loss
= min(4,) limits minority gradients.
Rare errors matter without unstable minority gradients.
2
Morphology-preserving augmentation
amplitude scaling, := small time shift, b := baseline shift for rare beats, := small noise
Noise and small shifts preserve the ECG beat shape.
3
Tested sampler: keep shuffle
Weighted and balanced mini-batches overcorrected.
Natural shuffle retained 95.3% test accuracy.
Quantization preserves per-class F1
3. Full-int8 compression keeps model quality
Representative-data calibration quantizes weights, activations, inputs, and outputs to int8 for TensorFlow Lite Micro.
q = clip(round( ; x ≈ s(q - z)
Model Size
Chart: 
| Float32 | INT8
Model size (KiB) | 88.2 | 23
-73.9% size | -0.14 percentage points accuracy
INT8 normalized confusion matrix
Predicted class
Class S remains hardest: 37% are confused with normal beats.
Deployment path
Float32 CNN
90,361 B
Full INT8 TFLite
23,576 B
ESP32 + TFLM
52.09 ms / beat
80 KiB tensor arena | full-int8 input/output | real MIT-BIH beats
Prototype scope
Validated on stored test beats. Live ADC acquisition, heartbeat segmentation, patient-wise clinical validation, and confidence handling remain future work.
TAKEAWAY
Full-int8 quantization is the deployment sweet spot: 23 KiB, 95.1% accuracy, and 52.09 ms ESP32 inference.
MIT-BIH heartbeat classification | Academic prototype - not a medical device
Chart: 
| N | S | V | F | Q
Float32 | 0.974 | 0.62 | 0.866 | 0.609 | 0.957
INT8 | 0.973 | 0.611 | 0.856 | 0.633 | 0.954
N
S
V
F
Q
N
0.96
0.01
0.02
0.01
0.00
S
0.37
0.56
0.04
0.01
0.01
V
0.02
0.00
0.95
0.02
0.00
F
0.10
0.00
0.09
0.81
0.00
Q
0.02
0.00
0.01
0.00
0.97
Notes: [Sources]
- Luka poster reference: C:/Users/alext/Documents/heidelberg/2Semester/AP_NN/ECG_Model_Compression_A0_Poster.pdf
- Dataset and class definitions: MIT-BIH Arrhythmia Database, PhysioNet, https://physionet.org/content/mitdb/
- Beat representation: Kachuee et al. (2018), ECG Heartbeat Classification, https://doi.org/10.1109/ICHI.2018.00092
- Final full-test metrics and model size: results/final_cap4_comparison/baseline_vs_int8_summary.md
- ESP32 latency and hardware validation: results/esp32_final_cap_4/hardware_run_25_samples.md
- Representative-beat image: output/pdf/8QmZg-representative-model-inputs-one-real-187-sample-beat-per-class-.png
[/Sources]