## Slide 1
Tiny ECG Classification on ESP32
A 73.9% smaller full-int8 CNN with 95.1% test accuracy
Aleksandar Toslev | Luka Zotovikj
Heidelberg University | Beginner's Practical Neural Networks from Scratch | 2026
FROM-SCRATCH CNN / TFLITE MICRO
95.12%
INT8 TEST ACCURACY
73.9%
SMALLER MODEL
52 ms
ESP32 INFERENCE / BEAT
1. Heartbeat data are highly imbalanced
Five heartbeat types must be separated from 187-point ECG segments. Normal beats dominate training, so overall accuracy alone can hide minority-class failure.
Representative normalized beats
Chart: 
N Normal
S Supraventricular
V Ventricular
F Fusion
Q Unknown
Training class distribution
Chart: 
| N | S | V | F | Q
Samples | 61600 | 1889 | 4920 | 545 | 5466
Class F has 113x fewer examples than class N.
2. Compact CNN, explicit imbalance controls
The complete forward pass, backward pass, weighted loss, and Adam updates are implemented in NumPy. Keras is used only as an export bridge.
11,173 trainable parameters
187 x 1 ECG beat
normalized heartbeat segment
Three convolution blocks
16 (k=7) -> 32 (k=5) -> 64 (k=3)
Global average pooling
small representation, no large flatten layer
Dense 32 + dropout
compact nonlinear classifier
Five-class softmax
N / S / V / F / Q
Three complementary strategies
1
Capped class-weighted loss
Inverse-frequency penalties, capped at 4 to avoid unstable minority gradients.
2
Mild rare-class augmentation
Noise, amplitude scaling, baseline shift, and small time shifts preserve beat shape.
3
Sampling controls
Natural shuffle, inverse-frequency weighted sampling, or balanced mini-batches.
Quantization preserves per-class F1
Chart: 
| N | S | V | F | Q
Float32 | 0.974 | 0.62 | 0.866 | 0.609 | 0.957
INT8 | 0.973 | 0.611 | 0.856 | 0.633 | 0.954
3. Full-int8 compression keeps model quality
Representative-data calibration quantizes weights, activations, inputs, and outputs to int8 for TensorFlow Lite Micro.
Model Size
Chart: 
| Float32 | INT8
Size (KiB) | 88.2 | 23
-73.9% size | -0.14 percentage points accuracy
INT8 normalized confusion matrix
N
N
S
S
V
V
F
F
Q
Q
0.96
0.01
0.02
0.01
0.00
0.37
0.56
0.04
0.01
0.01
0.02
0.00
0.95
0.02
0.00
0.10
0.00
0.09
0.81
0.00
0.02
0.00
0.01
0.00
0.97
Predicted class
Class S remains hardest: 37% are confused with normal beats.
Deployment path
Float32 CNN
90,361 B
Full INT8 TFLite
23,576 B
ESP32 + TFLM
52 ms / beat
80 KiB tensor arena | full-int8 input/output | real MIT-BIH beats
Prototype scope
Validated on stored test beats. Live ADC acquisition, heartbeat segmentation, patient-wise clinical validation, and confidence handling remain future work.
TAKEAWAY
Full-int8 quantization is the deployment sweet spot: 23 KiB, 95.1% accuracy, and real-time ESP32 inference.
github.com/alexToslev/ecg-model-compression
MIT-BIH heartbeat classification | Academic prototype - not a medical device
Project Goal Develop a 1D CNN from scratch in NumPy to accurately classify different heartbeat types, apply INT8 q quantization to reduce the model size, and optimize it for efficient deployment on an ESP32.
Project Goal
Stable convergence without clear overfitting
Notes: [Sources]
- C:/Users/alext/Documents/heidelberg/2Semester/ecg-model-compression/results/final_cap4_comparison/baseline_vs_int8_summary.csv - final float32 and int8 accuracy, loss, macro metrics, model size, tensor arena, and ESP32 latency.
- C:/Users/alext/Documents/heidelberg/2Semester/ecg-model-compression/results/final_cap4_comparison/comparison_plots/baseline_vs_int8_per_class_f1.png - final per-class F1 values used to recreate an editable chart.
- C:/Users/alext/Documents/heidelberg/2Semester/ecg-model-compression/results/final_cap4_comparison/quantized_plots/int8_confusion_matrix_normalized.png - normalized final int8 confusion values used to recreate an editable matrix.
- C:/Users/alext/Documents/heidelberg/2Semester/ecg-model-compression/results/improved_cnn_scratch/metrics.json - training class counts, final architecture, parameter count, and augmentation configuration.
- C:/Users/alext/Documents/heidelberg/2Semester/ecg-model-compression/src/models/cnn1d.py - from-scratch CNN architecture and weighted softmax-cross-entropy implementation.
- C:/Users/alext/Documents/heidelberg/2Semester/ecg-model-compression/src/train_cnn.py - capped balanced class weights, rare-class augmentation, and shuffle/weighted/balanced sampling implementations.
- C:/Users/alext/Documents/heidelberg/2Semester/ecg-model-compression/src/compression/quantize_tflite.py - full-integer TensorFlow Lite conversion and representative-dataset calibration.
- C:/Users/alext/Documents/heidelberg/2Semester/AP_NN/ecg-classification/ecg-classification/main/main_functions.cc - ESP32 TensorFlow Lite Micro tensor arena, inference, timing, and output handling.
- C:/Users/alext/Documents/heidelberg/2Semester/ecg-model-compression/data/processed/mitbih_test.csv - local ECG beat segments used only to render representative editable signal charts.
[/Sources]